## Slide 1
OBC
OBC
OBC
gnd
L
N
gnd
L
N
gnd
L
N
gnd
L1
L2
L3
200A FUSE
200A FUSE
B+
B-
10mm^2 cable
10mm^2 cable
95mm^2 cable
95mm^2 cable
Proximity Pilot PP (CC)
Control Pilot CP
CANBus
PP/CC and CP lines are connected to one of the OBC units only
OBC monitors CC/PP and CP lines according to IEC62196 and detects the plug state and allowable charging current. This information is then communicated over the CANBus to the vehicle control system (VCU).
Is it OK for all OBC to share the same fuses? Or does each OBC require its own set of fuses?
B+
B-
B-
B+
B+
B-